CSE-379/479 Library
Nathan Fox

# [Chapter Number] General Purpose Timers

There are multiple different options that can be used when enabling the general, though most of them are considered advanced. As such, these advanced options will be contained within a struct called timer_options. These options will include things like connecting the GPT (general purpose timer) module to other modules, such as the UDMA or PWM modules. By default, the timer_cinit function will require the following fields:
- Timer number enum
  - 16/32 bit timers are timer_0 to timer_5, 32/64 bit timers are called wtimer_0 to wtimer_5
- Load value (uint32_t)
- Timer width
  - Valid options are 16/32 for timer_0 to timer_5, and 32/64 for wtimer_0 to wtimer_5
- Direction
  - Positive number for counting up, negative number for counting down
- Interrupt
  - Bool, true to enable an interrupt
- Timer_mode enum
  - One shot mode, periodic, RTC, etc. Refer to Table 11-3 on page 708 of the TM4C123GH6PM documentation for more information.
- Timer_options struct
  - Additional options described on page [UNDEF]. If no additional options are desired, pass in a struct topt with the enabled field set to false.